# Bringing The Greenhouse Effect Down To Earth

Purpose: To compare the amount of Carbon Dioxide (CO2) in four different sources of gases.

Materials:

(Enough for each team of two or four students)
5 vials or test tubes
A graduated cylinder
A funnel straw
A marble-size piece of modeling clay
4 different colored balloons
4 twist-ties
A narrow-necked bottle (the neck should be narrow enough for a balloon to fit over it)
A dropping bottle of bromthymol blue indicator solution
A dropping bottle of dilute household ammonia (1 part ammonia to 50 parts distilled water)
100 mL vinegar
5 mL baking soda
Safety goggles for wear at all times

Lab Procedure:

1. Add 5 mL of water and 3 drops of bromthymol blue indicator solution to each vial or test tube. Label the vials A, B, C, D, and Control.

2. Fill each balloon until it has an 8 inch diameter.

Sample A (Ambient Air) - Use a tire pump to inflate the balloon to the required diameter. Twist the rubber neck of the balloon and fasten it shut with a twist tie. The tie should be at least 1 cm from the opening of the balloon. Record the color of the balloon used for this sample.

Sample B (Human Exhalation) - Have one team member blow up a balloon to the required diameter. Twist and tie the balloon, and record balloon color.

Sample C (Automobile Exhaust) - Your teacher will supply you with this balloon. Record the color.

Sample D (Nearly pure CO2) - Put 100 mL of vinegar in the narrow-necked bottle. Using a funnel, add 5 mL of baking soda. Let the mixture bubble for 3 seconds to drive the air out, then slip the balloon over the neck of the bottle. Inflate the balloon to the proper diameter. Twist, tie, and record the color.

3. Soften the clay and wrap it around one end of the straw to make a small airtight collar that will fit into the neck of a balloon. The collar should look like a cone with the straw in its middle, and should be large enough to plug the neck of the balloon.

4. Pick up Balloon A. Keeping the tie on it, slip the balloon's neck over the clay collar and hold it against the collar to make an airtight seal. Place the other end of the straw into the vial of water and bromthymol blue labelled A. Have another partner remove the tie on the balloon and slowly untwist the balloon. Keeping the neck of the balloon pinched to control the flow of gas, gently squeeze the balloon so the gas slowly bubbles through the solution.

5. Repeat the same procedure with the other balloons and their respective vials. In some cases, the bromthymol blue solution will change color, from blue to yellow, indicating the presence of carbonic acid formed from CO2.

6. Analyze each of the samples by titrating them with drops of dilute ammonia. Ammonia neutralizes the carbonic acid. The bromthymol blue will return to a blue color when all the acid has reacted. Add drops of ammonia to each of the samples that turned yellow, carefully counting the number of drops needed until they are about the same color as your control. Record the results.

Your grade will be determined by your Data collection table and Answer the review questions.

- Why didn't the ambient air sample not turn yellow? (The test isn't sensitive enough to detect low concentrations of CO2.)

- Carbon dioxide is a natural part of our atmosphere, but too much CO2 could make the Earth warmer through an increased greenhouse effect. Why is automobile exhaust a concern?

- What ways could you reduce the amount of CO2 you create?

- How could a city reduce the amount of CO2 they emit?

- What's more important, to develop and adapt cars with a new fuel that's safe for the environment or to improve public transportation systems?

- What alternative power sources could be used with cars? (Solar, electric, methanol.)

- Why might it be difficult for the public to start using an alternative source? (Car industry not mass-producing new cars, expense of buying new car, less power/speed than gas- powered car.)